## Slide 1: CS144 An Introduction to Computer Networks
Packet Switching
How a packet switch works (1)
Nick McKeown
Professor of Electrical Engineering
and Computer Science, Stanford University

## Slide 2: Outline
What does a packet switch look like?
What does a packet switch do?
  Ethernet switch
  Internet router
How address lookup works
  Ethernet switch
  Internet router

## Slide 3: Generic Packet Switch
Lookup
Address
Data
H
Destination
Address
Forwarding
Table
Egress link
Queue
Packet
Buffer
Memory
Update
Header

## Slide 4: Generic Packet Switch
Lookup
Address
Update
Header
Forwarding
Table
Lookup
Address
Update
Header
Forwarding
Table
Lookup
Address
Update
Header
Forwarding
Table
Queue
Packet
Buffer
Memory
Queue
Packet
Buffer
Memory
Queue
Packet
Buffer
Memory
Data
H
Data
H
Data
H

## Slide 5: Ethernet Switch
Examine the header of each arriving frame.
If the Ethernet DA is in the forwarding table, forward the frame to the correct output port(s).
If the Ethernet DA is not in the table, broadcast the frame to all ports (except the one through which the frame arrived).
Entries in the table are learned by examining the Ethernet SA of arriving packets.

## Slide 6: Internet Router
If the Ethernet DA of the arriving frame belongs to the router, accept the frame. Else drop it.
Examine the IP version number and length of the datagram.
Decrement the TTL, update the IP header checksum.
Check to see if TTL == 0.
If the IP DA is in the forwarding table, forward to the correct egress port(s) for the next hop.
Find the Ethernet DA for the next hop router.
Create a new Ethernet frame and send it.

## Slide 7: Basic Operations
Lookup Address: How is the address looked up in the forwarding table?
Switching: How is the packet sent to the correct output port?

## Slide 8: Lookup Address: Ethernet
Ethernet addresses (in a switch)
Methods
  Store addresses in hash table (maybe 2-way hash)
  Look for exact match in hash table
Match | Action
Ethernet DA = 0xA8B72340E678 | Forward to port 7
Ethernet DA = 0xB3D22571053B | Forward to port 3
… | …

## Slide 9: Lookup Address: IP
IP addresses (in a router)
Lookup is a longest prefix match, not an exact match
Match | Action
IP DA = 127.43.57.99 | Forward to 56.99.32.16
IP DA = 123.66.44.X | Forward to 22.45.21.126
IP DA = 76.9.X.X | Forward to 56.99.32.16
… | …

## Slide 10: Longest prefix match
128.9.16.0/21
128.9.172.0/21
128.9.176.0/24
0
232-1
128.9.0.0/16
142.12.0.0/19
65.0.0.0/8
128.9.16.14
65.14.24.120
Routing lookup: Find the longest matching prefix (aka the most specific route) among all prefixes that match the destination address.

## Slide 11: Longest prefix match lookup Binary tries
0
1
Entry | Prefix
a | 00001
b | 00010
c | 00011
d | 001
e | 0101
f | 011
g | 100
h | 1010
i | 1100
j | 11110000
e
f
g
h
i
j
d
a
b
c

## Slide 12: Longest prefix match lookup Ternary Content Addressable Memory (TCAM)
Entry | Prefix
a | 00001
b | 00010
c | 00011
d | 001
e | 0101
f | 011
g | 100
h | 1010
i | 1100
j | 11110000
Entry | Prefix
a | 00001XXX 11111000
b | 00010XXX 11111000
c | 00011XXX 11111000
d | 001XXXXX 11100000
e | 0101XXXX 11110000
… | …
j | 11110000 11111111
Binary value
+ Mask
Routing lookup: Compare address against every masked entry at the same time.

## Slide 13: Lookup Address: Generic
Generic or abstract lookups: <Match, Action>
Generalization of lookups and forwarding action in switches, routers, firewalls, etc.
Match | Action
IP DA = X | Forward to port 7
Eth DA = Y AND IP DA = Z | Drop packet

## Slide 14: Summary
Packet switches perform two basic operations:
  Lookup addresses in a forwarding table
  Switching to the correct egress port
At a high level, Ethernet switches and Internet routers perform similar operations
Address lookup is very different in switches and routers.